Protocol for control of vacuum embedded system
in Compass tokamak

November 2009
Tiago Valeriano

v. 2.0.0

Schematic of controlled hardware

The controlled hardware consists of a vacuum stand with: valves, pumps and gauges.

General flow of messages
The basic unit of exchanged information is the telegram described in the next section.
The embedded computer (pic microprocessor) usually just responds to queries. It will only send a telegram by its own initiative if a problem occurs.
The codac part of the system must be ready to receive error messages, as well as the responses to any issued queries.

Format of the telegram
##### Query
OPERATOR	ID_NUMBER	DATA (optional)	CHECKSUM	(cr)
3 bytes	1 byte	variable length	3 bytes	1 byte

Minimum length = 8 bytes

##### Response
OPERATOR	ID_NUMBER	RESPONSE_STATUS	DATA (optional)	CHECKSUM	(cr)
3 bytes	1byte	1 byte	variable length	3 bytes	1 byte

Minimum length = 9 bytes

##### Explanation of fields
OPERATOR - three numerical characters between 0 and 9 (ascii code 48 to 57). Defines a number between 0 and 999.
ID_NUMBER - one byte. Can be any value. The response will have the same value in this field as the query. The value zero should be avoided, as it is reserved for warning messages originated by the pic.
DATA - can be any sequence of bytes of any length, limited only by the buffers of the pic.
RESPONSE_STATUS - one readable byte (ascii code greater than 31).
CHECKSUM - three numerical characters between 0 and 9 (ascii code 48 to 57). This field is explained in section 5.
(cr) - termination character. Is always a carriage return (0x0D).

##### Notes:
The number of available operators is limited to 1000 (000 to 999).
If the field RESPONSE_STATUS is not OP_OK, the telegram will have no DATA field.
The possible codes for RESPONSE_STATUS are described in section 5.
##### Example query
Character					Ascii code
1	2	3	A	2	1	5	(cr)		49	50	51	65	50	49	53	13
OPERATOR			ID	CHECKSUM					OPERATOR			ID	CHECKSUM

##### Example response
Character					Ascii code
1	2	3	A	p	!	1	0	4	(cr)		49	50	51	65	112	33	49	48	52	13
OPERATOR			ID	RS	D	CHECKSUM					OPERATOR			ID	RS	D	CHECKSUM

OPERATOR field
1. OP_OPEN_3V1
2. OP_CLOSE_3V1
3. OP_OPEN_1V1
4. OP_CLOSE_1V1
5. OP_OPEN_2V1
6. OP_CLOSE_2V1
7. OP_OPEN_1V3
8. OP_CLOSE_1V3

The response to these operators doesn't have DATA field.

Example query
OP_OPEN_3V1	#	CHECKSUM	(cr)

Example responses
OP_OPEN_3V1	#	OP_OK	CHECKSUM	(cr)

1. OP_START_TMP1
2. OP_STOP_TMP1

1. OP_START_TMP2
2. OP_STOP_TMP2

1. OP_START_ROTARY
2. OP_STOP_ROTARY

Example query
OP_START_TMP1	#	CHECKSUM	(cr)

Example responses
OP_START_TMP1	#	OP_OK	CHECKSUM	(cr)

OP_SEND_CUSTOM_MSG_ICPCON_BUS

If RESPONSE_STATUS is OP_OK, then DATA field has the message returned by the ICPCON bus.
If RESPONSE_STATUS is not OP_OK, the telegram will have no DATA field.
The DATA field of the query telegram should contain the message to be sent to the ICPCON bus.

Example query
OP_SEND_CUSTOM_MSG_ICPCON_BUS	#	data to be sent to the ICPCON bus	CHECKSUM	(cr)

Example responses
OP_SEND_CUSTOM_MSG_ICPCON_BUS	#	OP_NO_RESPONSE_FROM_ICPCON_BUS	CHECKSUM	(cr)

OP_SEND_CUSTOM_MSG_ICPCON_BUS	#	OP_OK	data returned by ICPCON bus	CHECKSUM	(cr)

OP_SEND_CUSTOM_MSG_PFEIFFER_BUS

If RESPONSE_STATUS is OP_OK, then DATA field has the message returned by the PFEIFFER bus.
If RESPONSE_STATUS is not OP_OK, the telegram will have no DATA field.
The DATA field of the query telegram should contain the message to be sent to the PFEIFFER bus.

Example query
OP_SEND_CUSTOM_MSG_PFEIFFER_BUS	#	data to be sent to the PFEIFFER bus	CHECKSUM	(cr)

Example responses
OP_SEND_CUSTOM_MSG_PFEIFFER_BUS	#	OP_NO_RESPONSE_FROM_PFEIFFER_BUS	CHECKSUM	(cr)

OP_SEND_CUSTOM_MSG_PFEIFFER_BUS	#	OP_OK	data returned by PFEIFFER bus	CHECKSUM	(cr)

OP_GET_GAUGES_ERROR_COUNT

The DATA field is 20 bytes long and contains the error counts of the pfeiffer gauges.

Example query
OP_GET_ERROR_COUNT_TG1	#	CHECKSUM	(cr)

Example response
OP_GET_ERROR_COUNT_TG1	#	OP_OK	1	1	1	1	1	2	2	2	2	2

3	3	3	3	3	4	4	4	4	4	CHECKSUM	(cr)

This means that the error count for gauge TG1 is 11111, for gauge 1G1 is 22222, for gauge 2G1 is 33333 and for gauge 1G3 is 44444 errors.

OP_GET_TMP_ERROR_COUNT

The DATA field is 10 bytes long and contains the error counts of the turbo pumps.

Example query
OP_GET_TMP_ERROR_COUNT	#	CHECKSUM	(cr)

Example response
OP_GET_TMP_ERROR_COUNT	#	OP_OK	1	1	1	1	1	2	2	2	2	2	CHECKSUM	(cr)

This means that the error count for gauge TG1 is 11111, for gauge 1G1 is 22222, for gauge 2G1 is 33333 and for gauge 1G3 is 44444 errors.

OP_GET_ICPCONS_ERROR_COUNT

The DATA field is 25 bytes long and contains the error counts of the 5 icpcon modules.

Example query
OP_GET_ICPCONS_ERROR_COUNT	#	CHECKSUM	(cr)

Example response
OP_GET_ICPCONS_ERROR_COUNT	#	OP_OK	1	1	1	1	1	2	2	2	2	2

3	3	3	3	3	4	4	4	4	4	5	5	5	5	5	CHECKSUM	(cr)

This means that the error count for ICPCON 1 is 11111, for ICPCON 2 is 22222 and so on.

OP_GET_TMP_OPERATING_HOURS

The DATA field is 12 bytes long and contains the accumulated hours of pumping of the turbo pumps.

Example query
OP_GET_TMP_OPERATING_HOURS	#	CHECKSUM	(cr)

Example response
OP_GET_TMP_OPERATING_HOURS	#	OP_OK	1	1	1	1	1	1	2	2	2	2	2	2	CHECKSUM	(cr)

This means that the TMP 1 has operated 111111 hours and TMP 2 has operated 222222 hours.

1. OP_RESET_TMP_ERROR_COUNT
2. OP_RESET_GAUGES_ERROR_COUNT
3. OP_RESET_ICPCONS_ERROR_COUNT

Example query
OP_RESET_TMP_ERROR_COUNT	#	CHECKSUM	(cr)

Example response
OP_RESET_TMP_ERROR_COUNT	#	OP_OK	CHECKSUM	(cr)

1. OP_DEGAS_TG1
2. OP_DEGAS_1G1

Example query
OP_DEGAS_TG1	#	CHECKSUM	(cr)

Example response
OP_DEGAS_TG1	#	OP_OK	CHECKSUM	(cr)

1. OP_SWITCH_OFF_KK_SENSOR_2G1
2. OP_SWITCH_ON_KK_SENSOR_2G1

1. OP_SWITCH_OFF_FILAMENT_TG1
2. OP_SWITCH_ON_FILAMENT_TG1

1. OP_SWITCH_OFF_FILAMENT_1G1
2. OP_SWITCH_ON_FILAMENT_1G1

Example query
OP_SWITCH_OFF_KK_SENSOR_2G1	#	CHECKSUM	(cr)

Example response
OP_SWITCH_OFF_KK_SENSOR_2G1	#	OP_OK	CHECKSUM	(cr)

OP_GET_ALL_DATA

The DATA field is 73 bytes long and contains the full state of the system.
Example query
OP_GET_ALL_DATA	#	CHECKSUM	(cr)

Example response
OP_GET_ALL_DATA	#	OP_OK	data	CHECKSUM	(cr)

DATA field:

Field #	byte no	meaning	length
1	[0]	TG1 state	1
2	[1-6]	TG1 pressure	6
3	[7]	1G1 state	1
4	[8-13]	1G1 pressure	6
5	[14]	2G1 state	1
6	[15-20]	2G1 pressure	6
7	[21]	1G3 state	1
8	[22-27]	1G3 pressure	6
9	[28]	3V1 state	1
10	[29]	1V1 state	1
11	[30]	2V1 state	1
12	[31]	1V2 state	1
13	[32]	2V2 state	1
14	[33]	1V3 state	1
15	[34]	2V3 state	1
16	[35]	1V4 state	1
17	[36]	TMP1 state	1
18	[37-39]	TMP1 speed	3
19	[40-42]	TMP1 set speed	3
20	[43]	TMP2 state	1
21	[44-46]	TMP2 speed	3
22	[47-49]	TMP2 set speed	3
23	[50-52]	Glow discharge set speed	3
24	[53-55]	High vacuum set speed	3
25	[56]	Rotary state	1
26	[57]	Current mode	1
27	[58]	Requested mode	1
28	[59]	Pneumatic pressure	1
29	[60]	TMP cooling	1
30	[61]	Branch 1	1
31	[62]	Branch 2	1
32	[63-72]	PIC uptime	10

The possible states for TG1, 1G1, 2G1 and 1G3 (fields 1, 3, 5 and 7) are:
- OP_NO_RESPONSE_FROM_PFEIFFER_BUS
- OP_WRONG_SIZE_RESPONSE_FROM_PFEIFFER_BUS
- OP_BAD_FORMAT_RESPONSE_FROM_PFEIFFER_BUS
- OP_BAD_CRC_FROM_PFEIFFER_BUS
- OP_OK

The codification for the pressures (fields 2, 4, 6 and 8) is:
XYWZAB means X.YWZ * 10 ^ ( AB - 20 ) mBar

The possible states for 3V1, 1V1, 2V1, 1V2, 2V2, 1V3, 2V3 and 1V4 (fields 9 through 16) are:
- OP_VALVE_IS_CLOSED
- OP_VALVE_IS_OPENED
- OP_VALVE_IS_IN_ERROR
- OP_NO_RESPONSE_FROM_ICPCON_BUS
- OP_WRONG_SIZE_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_FORMAT_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_CRC_FROM_ICPCON_BUS

The possible states for TMP1and TMP2 (fields 17 and 20) are:
- OP_PUMP_IS_STOPPED
- OP_PUMP_IS_STARTED
- OP_PUMP_IS_ACCELERATING
- OP_PUMP_IS_STOPPING
- OP_NO_RESPONSE_FROM_ICPCON_BUS
- OP_WRONG_SIZE_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_FORMAT_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_CRC_FROM_ICPCON_BUS

The fields TMP1 SPEED and TMP2 SPEED (fields 18 and 19) indicate in ascii the current speed of the pumps TMP1 and TMP2. The unity is rotations per second.

The fields TMP1 SET SPEED and TMP2 SPEED (fields 21 and 22) indicate in ascii the programmed speed of the pumps TMP1 and TMP2. The unity is rotations per second.

The fields GLOW DISCHARGE SET SPEED and HIGH VACUUM SET SPEED (fields 23 and 24) indicate in ascii the programmed speed of the pumps TMP1 and TMP2 for the glow discharge and high vacuum modes, respectively. The unity is rotations per second.

The possible states for ROTARY STATE (field 25) are:
- OP_PUMP_IS_STOPPED
- OP_PUMP_IS_STARTED
- OP_PUMP_TRIPPED
- OP_NO_RESPONSE_FROM_ICPCON_BUS
- OP_WRONG_SIZE_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_FORMAT_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_CRC_FROM_ICPCON_BUS

The possible states for CURRENT MODE and REQUESTED MODE (fields 26 and 27) are:
- OP_STATE_IDLE
- OP_STATE_HIGH_VACUUM
- OP_STATE_PRIMARY_VACUUM
- OP_STATE_UNSAFE_MODE
- OP_STATE_STOP
- OP_STATE_GLOW_DISCHARGE

The possible states for PNEUMATIC PRESSURE (field 28) are:
- OP_PNEUMATIC_PRESSURE_OK
- OP_PNEUMATIC_PRESSURE_NOT_OK
- OP_NO_RESPONSE_FROM_ICPCON_BUS
- OP_WRONG_SIZE_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_FORMAT_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_CRC_FROM_ICPCON_BUS

The possible states for TMP COOLING (field 29) are:
- OP_TMP_COOLING_RUNNING
- OP_TMP_COOLING_STOPPED
- OP_NO_RESPONSE_FROM_ICPCON_BUS
- OP_WRONG_SIZE_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_FORMAT_RESPONSE_FROM_ICPCON_BUS
- OP_BAD_CRC_FROM_ICPCON_BUS

The possible states for BRANCH 1 and BRANCH 2 (field 30 and 31) are:
- OP_BRANCH_IS_INACTIVE
- OP_BRANCH_IS_ACTIVE

The field PIC UPTIME (field 32) represents in ASCII the number of seconds since the PIC was last reboot.

1. OP_GO_TO_STATE_IDLE
2. OP_GO_TO_STATE_HIGH_VACUUM
3. OP_GO_TO_STATE_PRIMARY_VACUUM
4. OP_GO_TO_STATE_UNSAFE_MODE
5. OP_GO_TO_STATE_STOP
6. OP_GO_TO_STATE_GLOW_DISCHARGE

Example query
OP_GO_TO_STATE_IDLE	#	CHECKSUM	(cr)

Example response
OP_GO_TO_STATE_IDLE	#	OP_OK	CHECKSUM	(cr)

1. OP_ACTIVATE_BRANCH_1
2. OP_ACTIVATE_BRANCH_2
3. OP_DEACTIVATE_BRANCH_1
4. OP_DEACTIVATE_BRANCH_2

Example query
OP_ACTIVATE_BRANCH_1	#	CHECKSUM	(cr)

Example response
OP_ACTIVATE_BRANCH_1	#	OP_OK	CHECKSUM	(cr)

List of all possible codes for RESPONSE_STATUS field
(fifth byte in response)

The RESPONSE_STATUS field can have the following values:
- OP_OK: the request operation was executed successfully.
- OP_NOT_OK: the requested operation was not executed successfully.
- OP_BAD_SIZE: the query didn't have the correct size.
- OP_BAD_FORMAT: the query was badly formated (ex: a non numeric value)
- OP_BAD_OPERATOR: the operator field was not numeric
- OP_CRC_ERROR: the query telegram had a CRC error.
- OP_NOT_IMPLEMENTED: the sent operator does not exist.
- OP_OPERATION_NOT_ALLOWED: the requested operation is not allowed in the present state (in "unsafe mode" all operations are allowed).
- OP_NO_RESPONSE_FROM_ICPCON_BUS: the ICPCON bus did not return an answer.
- OP_WRONG_SIZE_RESPONSE_FROM_ICPCON_BUS: the response from the ICPCON bus was too short.
- OP_BAD_FORMAT_RESPONSE_FROM_ICPCON_BUS: the delimiter character in the ICPCON response was not the expected one.
- OP_BAD_CRC_FROM_ICPCON_BUS: the ICPCON bus returned a messaged with a CRC error.
- OP_NO_RESPONSE_FROM_PFEIFFER_BUS: the PFEIFFER bus did not return an answer.
- OP_WRONG_SIZE_RESPONSE_FROM_PFEIFFER_BUS: the size of the response from the PFEIFFER bus was not the expected one.
- OP_BAD_FORMAT_RESPONSE_FROM_PFEIFFER_BUS: the delimiter character in the PFEIFFER response was not the expected one.
- OP_BAD_CRC_FROM_PFEIFFER_BUS: the PFEIFFER bus returned a messaged with a CRC error.

List of all possible codes for DATA field (sixth byte in response)

The DATA field can have the following values:
- OP_VALVE_IS_CLOSED: self explanatory
- OP_VALVE_IS_OPENED: self explanatory
- OP_VALVE_IS_IN_ERROR: the electrical contacts in the valve indicate a problem with the valve itself.
- OP_PUMP_IS_STOPPED: self explanatory
- OP_PUMP_IS_STARTING: the pump is accelerating (only for turbo molecular pumps)
- OP_PUMP_IS_STOPPING: the pump is stopping (only for turbo molecular pumps)
- OP_PUMP_IS_STARTED: self explanatory
- OP_PUMP_IS_IN_ERROR: the electrical contacts and the current detector in the pump indicate an error.
- OP_STATE_IDLE: indicates idle state: only interlock is working for protection of equipment.
- OP_STATE_HIGH_VACUUM: indicates high vacuum: rotary, roots and turbo pump working.
- OP_STATE_PRIMARY_VACUUM: indicates primary vacuum: rotary pump working and turbo pumps stopped.
- OP_STATE_UNSAFE_MODE: indicates unsafe mode: no interlock for protection of equipment and all operations allowed.
- OP_STOP_STATE: indicates stop state: all valves closed and pumps stopped.
- OP_STATE_GLOW_DISCHARGE: indicates glow discharge state: rotary on and turbo pumps working at predefined speed for glow discharge.
- OP_BRANCH_IS_ACTIVE: the branch (includes one turbo pump and one valve) of the vacuum system is working.
- OP_BRANCH_IS_INACTIVE: the branch (includes one turbo pump and one valve) of the vacuum system is closed.
- OP_PNEUMATIC_PRESSURE_OK: the pneumatic pressure for actuation of the valves is ok.
- OP_PNEUMATIC_PRESSURE_NOT_OK: there is no pneumatic pressure for actuation of the valves.
- OP_TMP_COOLING_RUNNING: the water is flowing in the cooling circuit of the turbo pumps.
- OP_TMP_COOLING_STOPPED: the water is not flowing in the cooling circuit of the turbo pumps.

Warning telegrams from pic

This section lists and explains the warning telegrams that the embedded micro processor may send to the codac, without being queried, in case any problem arises.

Example warning telegram
OP_ERR_PNEUMATIC_PRESSURE	(0)	CHECKSUM	(cr)

The embedded micro processor will send these warnings if it detects a problem in the system. The warning telegram will be sent to the codac if the problem occurs for more than 30 seconds and will be repeated every 131 seconds if the problem persists.

Possible codes for field OPERATOR are:
- OP_ERR_PNEUMATIC_PRESSURE: there is no pressure to actuate the pneumatic valves
- OP_ERR_TMP_COOLING: there is no water flow in the turbo pumps cooling circuit
- OP_ERR_VALVE_1V1: electrical contacts in valve 1V1 indicate that the valve is in a stale position
- OP_ERR_VALVE_2V1: electrical contacts in valve 2V1 indicate that the valve is in a stale position
- OP_ERR_VALVE_1V3: electrical contacts in valve 1V3 indicate that the valve is in a stale position
- OP_ERR_VALVE_1V2: electrical contacts in valve 1V2 indicate that the valve is in a stale position
- OP_ERR_VALVE_2V2: electrical contacts in valve 2V2 indicate that the valve is in a stale position
- OP_ERR_VALVE_1V4: electrical contacts in valve 1V4 indicate that the valve is in a stale position
- OP_ERR_VALVE_3V1: electrical contacts in valve 3V1 indicate that the valve is in a stale position
- OP_ERR_VALVE_2V3: electrical contacts in valve 2V3 indicate that the valve is in a stale position
- OP_ERR_PUMP_TMP1: electrical contacts and current detector in pump TMP1 indicate that an error is occurring in the pump
- OP_ERR_PUMP_TMP2: electrical contacts and current detector in pump TMP2 indicate that an error is occurring in the pump
- OP_ERR_ICPCON_BUS: an error occurred in the icpcon bus (pe: the bus returned no response to a query)
- OP_ERR_PFEIFFER_BUS: an error occurred in the pfeiffer bus (pe: the bus returned no response to a query)
- OP_MANUAL_INTERVENTION_NEEDED: because of valves 1V1 and 2V1, the vacuum system need to be filled with gas, to equalize the pressure or both sides of theses valves, or the valve 2V3 need to be open (manually)
- OP_ROTARY_PUMP_TRIP: the rotary is shutdown because the thermal protection circuit built in the pump was activated
- OP_ROTARY_PUMP_COOLING: the rotary pump was turned on, while it was cooling (this may damage the pump)

Checksum

The checksum at the end of the telegram consists of the sum of all other bytes in the message (except the termination character) modulo 256.
It is written using ascii characters.

Example telegram

Character
0	3	2	d	f	1	2	3	4	5	0	9	4	(cr)

Ascii code
48	51	50	100	102	49	50	51	52	53	48	57	52	13